## Slide 1: Fundamentals of Computer Architect
Presented by: Han Trung Dinh

## Slide 2: References and Evaluation
References:
  Kai H., Naresh J., Advanced Computer Architecture - Parallelism, Scalability, Programmability, Mcgraw-Hill, 2008
  John L. H., David A. P., Computer Architecture, A Quantitative Approach, 6th edition, Elsevier, 2019
  Ata E., Computer Systems - Digital Design, Fundamentals of Computer Architecture and Assembly Language, Springer, 2018
  Igor Z. Low-Level Programming - C, Assembly, and Program Execution on Intel® 64 Architecture, Apress 2017
  Larry D. P., Modern Assembly Language Programming with the ARM Processor, Elsevier, 2016
  Barry B. B., The Intel microprocessors - The Architecture, Programming, and Interfacing, 8th Edition, Prentice Hall, 2008
(*) Note that this course uses a lot of sources from the Internet
Evaluation:
  Projects/paper presentation/writing papers: 50%
  Final exam: 50%
Prerequisites:
  Students should have fundamental knowledge of Computer Architecture

## Slide 3: Introduction
Fig. 1.1 Growth in processor performance over 40 years (VAX-11/780 was introduced on 25 October 1977 at Digital Equipment Corporation (DEC))

## Slide 4: Classes of Computers
Fig. 1.2 A summary of the five mainstream computing classes and their system characteristics

## Slide 5: Classes of Computers (cont.)
Fig. 1.3 Costs rounded to nearest $100,000 of an unavailable system are shown by analyzing the cost of downtime

## Slide 6: Classes of Parallelism and Parallel Architectures
There are basically two kinds of parallelism
  Data-level parallelism (DLP): many data items can be operated concurrently
  Task-level parallelism (TLP): tasks can operate independently and largely in parallel
Computer hardware exploits these two parallelism as follows:
  Instruction-level parallelism (ILP) exploits DLP at modest levels with compiler help using pipelining and at medium levels using speculative execution
  Vector architectures, graphic processor units (GPUs), and multimedia instruction sets exploit DLP by applying a single instruction to a collection of data in parallel
  Thread-level parallelism (TLP) exploits either DLP or TLP in a tightly coupled hardware model that allows for interaction between parallel threads
  Request-level parallelism (RLP) exploits parallelism among largely decoupled tasks specified by the programmer or the operating system

## Slide 7: Classes of Parallelism and Parallel Architectures
Flynn (1966) suggested a simple way for classification
  Single instruction stream, single data stream (SISD)—This category is the uniprocessor. The programmer thinks of it as the standard sequential computer, but it can exploit ILP
  Single instruction stream, multiple data streams (SIMD)—The same instruction is executed by multiple processors using different data streams. SIMD computers exploit DLP by applying the same operations to multiple items of data in parallel
  Multiple instruction streams, single data stream (MISD)—No commercial multiprocessor of this type has been built to date, but it rounds out this simple classification
  Multiple instruction streams, multiple data streams (MIMD)—Each processor fetches its own instructions and operates on its own data, and it targets task-level parallelism

## Slide 8: Defining Computer Architecture
Determine what attributes are important for a new computer
Design a computer to maximize performance and energy efficiency while staying within cost, power, and availability constraints
  Instruction Set Architecture (ISA) design
  Functional organization
  Logic design
  Implementation (encompass integrated circuit design, packaging, power, and cooling)

## Slide 9: Instruction Set Architecture (ISA)
ISA serves as the boundary between the software and hardware
E.g.,
  80x86
  ARM (Advanced RISC Machine), 14.8 billion chips (2015)
  RISC-V, a modern RISC developed at the University of California, Berkeley

## Slide 10: RISC-V Registers
Fig. 1.4 RISC-V registers, names, usage, and calling conventions
Caller: volatile registers
Callee: non-volatile registers

## Slide 11: Subset of the instructions in RISC-V (1)
Fig. 1.5.1 Data transfer instructions in RISC-V

## Slide 12: Subset of the instructions in RISC-V (2)
Fig. 1.5.2 Arithmetic/logical instructions in RISC-V

## Slide 13: Subset of the instructions in RISC-V (3)
Fig. 1.5.3 Control instructions in RISC-V

## Slide 14: Subset of the instructions in RISC-V (4)
Fig. 1.5.4 Floating point instructions in RISC-V

## Slide 15: The base RISC-V instruction set architecture formats
R-type: for integer register-to-register operations, such as ADD, SUB…
I-type: for loads and immediate operations, such as LD and ADDI
B-type: for branches
J-type: for jump and link
S-type: for stores
U-type: for wide immediate instructions (LUI, AUIPC).
Fig. 1.6 RISC ISA Formats

## Slide 16: Growth in clock rate of microprocessors
Fig. 1.7 Clock rate improvement

## Slide 17: Amdahl’s Law
Amdahl’s Law states that the performance improvement to be gained from using some faster mode of execution is limited by the fraction of the time the faster mode can be used

## Slide 18: Amdahl’s Lawn (cont.)

## Slide 19: Amdahl’s Lawn (cont.)

## Slide 20: The Processor Performance Equation
CPU time for a program can then be expressed two ways
We can calculate the average number of clock cycles per instruction (CPI)
■ Clock cycle time—Hardware technology and organization
■ CPI—Organization and instruction set architecture
■ Instruction count—Instruction set architecture and compiler technology

## Slide 21: The Processor Performance Equation

## Slide 22: Computer Block Diagram
Fig. 1.8 Components of a modern computer
(a) Von Neumann Architecture
(a) Harvard Architecture

## Slide 23: Multicore Processor Architecture

## Slide 24: Disk Controller
IDE (integrated disk electronics), ~ 133 MB/s
SATA (Serial Advanced Technology Attachment), upto 6 GB/s
SCSI (small computer systems interface)

## Slide 25: Bus
ISA: Industry Standard Architecture
MCA: MicroChannel Architecture
VESA: Video Electronics Standard Association
PCI: Peripheral Component Interconnect

## Slide 26: USB architecture

## Slide 27: Memory hierarchy

## Slide 28: The 8086 through the Core2 microprocessor

## Slide 29: The physical memory systems of the 8086 family

## Slide 30: The physical memory systems of the 8086 family (cont.)

## Slide 31: Addressing Modes

## Slide 32: Examples of register-addressed instructions

## Slide 33: Examples of register indirect addressing

## Slide 35: Examples of base-plus-index addressing

## Slide 36: An example showing how the base-plus-index addressing
MOV DX,[ BX + DI]
Notice that memory address 02010H is accessed because DS = 0100H, BX = 100H, and DI = 0010H

## Slide 37: An example of assembly program

## Slide 38: What you have learned
Class of Computers
Defining Computer Architecture
Instruction Set Architecture
Amdahl’s Lawn
Processor Performance Equation
Computer Block Diagram
8086 family architect
Disk controller, bus, usb
Addressing modes
Assembly program example